VCE – Adjustable Vacuum Switches

TECHNICAL DATA

| Switch rating | 0,5(0,2)A / 48Vac-dc |
| --- | --- |
| Electrical connection | Push-on terminals 6,3x0,8 |
| Adjustment range | -200…-900 mbar |
| Max static pressure | 20 bar |
| Hysteresis | Fixed (but according to the set-point adjustment) |
| Operating temperature | -5°C ... +60°C |
| Contact (without pressure) | N.O. or N.C. |
| Body material | Brass |
| Diaphragm | NBR (standard) – other materials on request |
| Threads | Taper: G1/8” – G1/4” |
| Protection | IP00 (terminals) IP54 (with CAP1 and CAP10) |
| Mechanical life | 106 operations |
| Size | Body 24 AF Max. height 48 mm |
| Certifications and Approvals | - - |
| Options | Set-point adjustment rising Set-point adjustment falling |

PROTECTION CAPS

| CAP1 Protection: IP54 Material: NBR – FKM – EPDM | CAP10 Protection: IP54 Material: NBR |
| --- | --- |