PSM / PSP Series - Diaphragm/Piston Adjustable Pressure Switches Intrinsic Safety Execution

TECHNICAL DATA

| Type approval certificate | ATEX - II 1 G EEx ia IIC T6 |
| --- | --- |
| INTRINSIC SAFETY PARAMETERS |  |
| Working temperature | -20°C to +70°C |
| Input voltage | Vi 30V |
| Input current | Ii 100mA |
| Max. input power | Pi 0.75W |
| Input capacity | Ci ~= 0 |
| Input inductance | Li ~= 0 |
| Electrical connection | DIN 43650 – PG09 (standard)/PG11 |
| Adjusting range | 0,2…300 bar |
| Max static pressure | 600 bar |
| Hysteresis | Adjustable 10% to 30% set-point |
| Contact (without pressure) | SPDT |
| Body material | Tropicalized Steel (standard) 303 Stainless Steel – stal nierdzewna 316 |
| Diaphragm/Piston seal | NBR (standard) – HNBR - FKM – Silicone – EPDM – Neoprene – Stainless Steel |
| Threads | Parallel: G1/8" – G1/4" – M10x1 – M12x1.5 Taper: 1/8 NPT |
| Protection | IP65 |
| Mechanical life | 106 operations |
| Size | Body 27 AF - Max height 85mm |
| Options | Set-point adjustment rising – Set-point adjustment falling – Factory set-point and hysteresis adjustment – Gold contacts – Degreasing for oxygen applications – Gas test – High pressure execution – Special thread connections |

VSM Series - Vacuum Switches Intrinsic Safety Executio

TECHNICAL DATA

| Type approval certificate | ATEX - II 1 G EEx ia IIC T6 |
| --- | --- |
| INTRINSIC SAFETY PARAMETERS |  |
| Working temperature | -20°C to +70°C |
| Input voltage | Vi 30V |
| Input current | Ii 100mA |
| Max. input power | Pi 0.75W |
| Input capacity | Ci ~= 0 |
| Input inductance | Li ~= 0 |
| Electrical connection | DIN 43650 – PG09 (standard)/PG11 |
| Adjusting range | -100…-900 mbar |
| Max static pressure | 20 bar |
| Hysteresis | Adjustable 10% to 30% set-point |
| Contact (without pressure) | SPDT |
| Body material | Tropicalized Steel (standard) 303 Stainless Steel – stal nierdzewna 316 |
| Diaphragm | NBR (standard) – HNBR - FKM – Silicone – EPDM – Neoprene |
| Threads | Parallel: G1/8" – G1/4" – M12x1.5 |
| Protection | IP65 |
| Mechanical life | 106 operations |
| Size | Body 27 AF - Max height 85mm |
| Options | Set-point adjustment rising – Set-point adjustment falling – Factory set-point and hysteresis adjustment – Gold contacts – Degreasing for oxygen applications – Gas test |

PMC / PPC Series - Diaphragm/Piston Adjustable Pressure Switches Intrinsic Safety Execution

TECHNICAL DATA

| Type approval certificate | ATEX - II 1 G EEx ia IIC T6 |
| --- | --- |
| INTRINSIC SAFETY PARAMETERS |  |
| Working temperature | -20°C to +70°C |
| Input voltage | Vi 30V |
| Input current | Ii 100mA |
| Max. input power | Pi 0.75W |
| Input capacity | Ci ~= 0 |
| Input inductance | Li ~= 0 |
| Electrical connection | DIN 43650 – PG09 |
| Adjusting range | 0,15…300 bar |
| Max static pressure | 600 bar |
| Hysteresis | £ 30% set-point adjustment |
| Contact (without pressure) | SPDT |
| Body material | Anodized aluminium Flange: nickel-plated steel |
| Diaphragm/Piston seal | NBR |
| Threads | Taper: G1/8" – G1/4" |
| Protection | IP65 |
| Mechanical life | 106 operations |
| Size | Body 30x30 + connector 37x30 Height 58mm; with connector max. 78mm |
| Options | Set-point adjustment rising – Set-point adjustment falling – Gold contacts – Degreasing for oxygen applications – Execution with 2 SPDT contacts |

PPCF Series - Piston Adjustable Pressure Switches Intrinsic Safety Execution

TECHNICAL DATA

| Type approval certificate | ATEX - II 1 G EEx ia IIC T6 |
| --- | --- |
| INTRINSIC SAFETY PARAMETERS |  |
| Working temperature | -20°C to +70°C |
| Input voltage | Vi 30V |
| Input current | Ii 100mA |
| Max. input power | Pi 0.75W |
| Input capacity | Ci ~= 0 |
| Input inductance | Li ~= 0 |
| Electrical connection | DIN 43650 – PG09 |
| Adjusting range | 30…300 bar |
| Max static pressure | 600 bar |
| Hysteresis | £ 30% set-point adjustment |
| Contact (without pressure) | SPDT |
| Body material | Anodized aluminium Flange: nickel-plated steel |
| Piston seal | NBR |
| Threads | G1/4" female |
| Protection | IP65 |
| Mechanical life | 106 operations |
| Size | Body 30x30 + connector 37x30 Height 72mm; with connector max. 92mm |
| Options | Set-point adjustment rising – Set-point adjustment falling – Gold |

PML / PPL Series – Diaphragm/Piston Adjustable Pressure Switches Intrinsic Safety Execution

TECHNICAL DATA

| Type approval certificate | ATEX - II 1 G EEx ia IIC T6 |
| --- | --- |
| INTRINSIC SAFETY PARAMETERS |  |
| Working temperature | -20°C to +70°C |
| Input voltage | Vi 30V |
| Input current | Ii 100mA |
| Max. input power | Pi 0.75W |
| Input capacity | Ci ~= 0 |
| Input inductance | Li ~= 0 |
| Electrical connection | DIN 43650 – PG09 |
| Adjusting range | 0,5…350 bar |
| Max static pressure | 600 bar |
| Hysteresis | £ 30% set-point adjustment |
| Contact (without pressure) | SPDT |
| Body material | Anodized aluminium Connection: steel |
| Diaphragm/Piston seal | NBR |
| Threads | G1/4" female |
| Protection | IP65 |
| Mechanical life | 106 operations |
| Size | Body 30x30 + connector 48x30 Max height 95mm |
| Options | Set-point adjustment rising – Set-point adjustment falling – Gold |