LEM5 – Low-cost Level Switches

TECHNICAL DATA

| Materials of construction | Stem: Nylon Float: NBR |
| --- | --- |
| Punkt aktywacji | 1 lub 2 with N.O. – N.C. – SPDT contacts |
| Mocowanie | G1/4” |
| Electrical connection | 500mm leads (standard) |
| Switching capacity | N.C./N.O. contacts - 60W/VA SPDT contacts – 30W/VA |
| Current | N.C./N.O. contacts - 0,8A (resistive) SPDT contacts - 0,5A (resistive) |
| Max voltage | 220V – 50Hz |
| Temperature range | -10°C +80°C |
| Max. ciśnienie | 5 bar |
| Fluid specific weight | ³ 0.7 |
| Fluid viscosity | Max 150 cSt |
| Certification and approvals | - - |
| Size | LEM5CN - 82mm LEM5LN/LEM5M - 146mm |

L

EM6  Low-cost Level Switches

TECHNICAL DATA

| Materials of construction | Stem: Nylon Float: NBR |
| --- | --- |
| Punkt aktywacji | 1 with N.O. – N.C. – SPDT contacts |
| Mocowanie | G1/8” |
| Electrical connection | 500mm leads (standard) |
| Switching capacity | N.C. contacts – 10W/VA SPDT/N.O. contacts – 3W/VA |
| Current | N.C. contacts - 0,5A (resistive) SPDT/N.O. contacts - 0,25A (resistive) |
| Max voltage | N.C. contacts: 220V – 50Hz SPDT/N.O. contacts: 175Vdc |
| Temperature range | -10°C +80°C |
| Max. ciśnienie | 5 bar |
| Fluid specific weight | ³ 0.7 |
| Fluid viscosity | Max 150 cSt |
| Certification and approvals | - - |
| Size | LEM6CN – 65mm |

LEM5..A - Non-toxic Level Switches

TECHNICAL DATA

| Materials of construction | Stem: Hostaform Float: stal nierdzewna 316 |
| --- | --- |
| Punkt aktywacji | 1 lub 2 with N.O. – N.C. – SPDT contacts |
| Mocowanie | G1/4” |
| Electrical connection | 500mm leads (standard) |
| Switching capacity | N.C./N.O. - 60W/VA SPDT contacts – 30W/VA |
| Current | N.C./N.O. contacts - 0,8A (resistive) SPDT contacts - 0,5A (resistive) |
| Max voltage | 220V – 50Hz |
| Temperature range | -10°C +80°C |
| Max. ciśnienie | 5 bar |
| Fluid specific weight | ³ 0.7 |
| Fluid viscosity | Max 150 cSt |
| Certification and approvals | - - |
| Size | LEM5CA – 82mm LEM5LA/LEM5MA – 146mm |

LEM6..A - Non-toxic Level Switches

TECHNICAL DATA

| Materials of construction | Stem: Hostaform Float: stal nierdzewna 316 |
| --- | --- |
| Punkt aktywacji | 1 with N.O. – N.C. – SPDT contacts |
| Mocowanie | G1/8” |
| Electrical connection | 500mm leads (standard) |
| Switching capacity | N.C. contacts - 10W/VA SPDT/N.O. contacts – 3W/VA |
| Current | N.C. contacts - 0,5A (resistive) SPDT/N.O. contacts - 0,25A (resistive) |
| Max voltage | N.C. contacts: 220V – 50Hz SPDT/N.O. contacts: 175Vdc |
| Temperature range | -10°C +80°C |
| Max. ciśnienie | 5 bar |
| Fluid specific weight | ³ 0.7 |
| Fluid viscosity | Max 150 cSt |
| Certification and approvals | - - |
| Size | LEM6CA – 65mm LEM6LA – 130mm |

LEM7 - Stainless Steel Low-cost Level Switches

TECHNICAL DATA

| Materials of construction | All stal nierdzewna 316 execution |
| --- | --- |
| Punkt aktywacji | 1 with N.O. – N.C. – SPDT contacts |
| Mocowanie | G1/8” |
| Electrical connection | 500mm leads (standard) |
| Switching capacity | N.C. contacts - 10W/VA SPDT/N.O. contacts – 3W/VA |
| Current | N.C. contacts - 0,5A (resistive) SPDT/N.O. contacts - 0,25A (resistive) |
| Max voltage | N.C. contacts: 220V – 50Hz SPDT/N.O. contacts: 175Vdc |
| Temperature range | -10°C +80°C |
| Max. ciśnienie | 10 bar |
| Fluid specific weight | ³ 0.7 |
| Fluid viscosity | Max 150 cSt |
| Certification and approvals | - - |
| Size | LEM7 – 70mm LEM7L – 115mm LEM7A – Bent stem execution |

LMD / LM - Low-cost Level Switches

TECHNICAL DATA

| Materials of construction | Stem: brass Float: NBR Fitting: brass |
| --- | --- |
| Punkt aktywacji | 1 with N.C. – N.O. – SPDT contacts |
| Mocowanie | LMD - G1/8” taper (male) LM – G1/8” taper (female) |
| Electrical connection | 500mm leads (standard) |
| Switching capacity | LMD1/LM1 - 60W/VA LMD2/LM2 - 30W/VA |
| Current | LMD1/LM1 - 0,8A (resistive) LMD2/LM2 - 0,5A (resistive) |
| Max voltage | 220V – 50Hz |
| Temperature range | -10°C +80°C |
| Max. ciśnienie | 10 bar |
| Fluid specific weight | ³ 0.7 |
| Fluid viscosity | 150 cSt |
| Certification and approvals | - - |
| Size | LMD - 82mm LM - 73mm |

LM1 / LM2 / LMM1 A-FA-TA - Level Switches with Stop Ring

TECHNICAL DATA

| Materials of construction | Stem: brass Float: NBR Mocowanie: anodized aluminium |
| --- | --- |
| Punkt aktywacji | LM1 – 1 actuation point N.C./N.O. contact LM2 – 1 actuation point SPDT contact LMM1 – 2 Punkt aktywacji/floats N.C./N.O. contacts |
| Mocowanie | A – M18x1,5 thread connection FA – Ø 52 flange TA – G1” thread connection |
| Electrical connection | DIN 43650 – PG09 – IP65 |
| Switching capacity | LM1/LMM1 - 60W/VA LM2 - 30W/VA |
| Current | LM1/LMM1 - 0,8A (resistive) LM2 - 0,5A (resistive) |
| Max voltage | 220V – 50Hz |
| Temperature range | -10°C +80°C |
| Max. ciśnienie | 10 bar |
| Fluid specific weight | ³ 0.7 |
| Fluid viscosity | 150 cSt |
| Certification and approvals | - - |
| Size | Max possible length 1500mm |

LM1 LA - LFA - Level Switches with LED

TECHNICAL DATA

| Materials of construction | Stem: brass Float: NBR Mocowanie: anodized aluminium |
| --- | --- |
| Punkt aktywacji | 1 with N.C. contact |
| Mocowanie | LA – M18x1,5 thread connection LFA – Ø 52 flange |
| Electrical connection | DIN 43650 – PG09 – IP65 |
| Switching capacity | 60W/VA |
| Current | 0,8A (resistive) |
| Max voltage | 220V – 50Hz |
| Temperature range | -10°C +80°C |
| Max. ciśnienie | 10 bar |
| Fluid specific weight | ³ 0.7 |
| Fluid viscosity | 150 cSt |
| Certification and approvals | - - |
| Size | Max possible length 1500mm LED voltage: 24Vdc/Vac 110Vac 220Vac |

LM1 / LM2 / LMM1 FPA - TPA - Level Switches with Stop Ring

TECHNICAL DATA

| Materials of construction | Stem: brass Float: NBR Mocowanie: thermoplastic |
| --- | --- |
| Punkt aktywacji | LM1 – 1 actuation point N.C./N.O. contact LM2 – 1 actuation point SPDT contact LMM1 – 2 Punkt aktywacji/floats N.C./N.O. contacts |
| Mocowanie | FPA – Ø 54 flange TPA – G1” thread connection |
| Electrical connection | DIN 43650 – PG09 – IP65 |
| Switching capacity | LM1/LMM1 - 60W/VA LM2 – 30W/VA |
| Current | LM1/LMM1- 0,8A (resistive) LM2 - 0,5A (resistive) |
| Max voltage | 220V – 50Hz |
| Temperature range | -10°C +80°C |
| Max. ciśnienie | 10 bar |
| Fluid specific weight | ³ 0.7 |
| Fluid viscosity | 150 cSt |
| Certification and approvals | - - |
| Size | Max possible length 1500mm |

LM1 / LM2 / LMM1 CFPA - CTPA - Level Switches

TECHNICAL DATA

| Materials of construction | Stem: brass Float: NBR Mocowanie: thermoplastic |
| --- | --- |
| Punkt aktywacji | LM1 – 1 actuation point N.C./N.O. contact LM2 – 1 actuation point SPDT contact LMM1 – 2 Punkt aktywacji N.C./N.O. contacts |
| Connection | CFPA – Ø 54 flange CTPA – G1” thread connection |
| Electrical connection | DIN 43650 – PG09 – IP65 |
| Switching capacity | LM1/LMM1 - 60W/VA LM2 – 30W/VA |
| Current | LM1/LMM1- 0,8A (resistive) LM2 - 0,5A (resistive) |
| Max voltage | 220V – 50Hz |
| Temperature range | -10°C +80°C |
| Max. ciśnienie | 10 bar |
| Fluid specific weight | ³ 0.7 |
| Fluid viscosity | 150 cSt |
| Certification and approvals | - - |
| Size | Max possible length 1500mm |

LM1 / LM2 / LMM1 FPA - TPA - Level Switches with Stop Ring

TECHNICAL DATA

| Materials of construction | Stem: brass Float: NBR Mocowanie: thermoplastic |
| --- | --- |
| Punkt aktywacji | LM1 – 1 actuation point N.C./N.O. contact LM2 – 1 actuation point SPDT contact LMM1 – 2 Punkt aktywacji/floats N.C./N.O. contacts |
| Mocowanie | FPA – Ø 54 flange TPA – G1” thread connection |
| Electrical connection | DIN 43650 – PG09 – IP65 |
| Switching capacity | LM1/LMM1 - 60W/VA LM2 – 30W/VA |
| Current | LM1/LMM1- 0,8A (resistive) LM2 - 0,5A (resistive) |
| Max voltage | 220V – 50Hz |
| Temperature range | -10°C +80°C |
| Max. ciśnienie | 10 bar |
| Fluid specific weight | ³ 0.7 |
| Fluid viscosity | 150 cSt |
| Certification and approvals | - - |
| Size | Max possible length 1500mm |

LM1 / LM2 / LMM1 CFPA - CTPA - Level Switches

TECHNICAL DATA

| Materials of construction | Stem: brass Float: NBR Mocowanie: thermoplastic |
| --- | --- |
| Punkt aktywacji | LM1 – 1 actuation point N.C./N.O. contact LM2 – 1 actuation point SPDT contact LMM1 – 2 Punkt aktywacji N.C./N.O. contacts |
| Connection | CFPA – Ø 54 flange CTPA – G1” thread connection |
| Electrical connection | DIN 43650 – PG09 – IP65 |
| Switching capacity | LM1/LMM1 - 60W/VA LM2 – 30W/VA |
| Current | LM1/LMM1- 0,8A (resistive) LM2 - 0,5A (resistive) |
| Max voltage | 220V – 50Hz |
| Temperature range | -10°C +80°C |
| Max. ciśnienie | 10 bar |
| Fluid specific weight | ³ 0.7 |
| Fluid viscosity | 150 cSt |
| Certification and approvals | - - |
| Size | Max possible length 1500mm |

LMA1 / LMA2 / LMMA1 FA - FIA - Bent Stem Level Switches

TECHNICAL DATA

| Materials of construction | FA – brass stem, NBR float, Mocowanie in anodized aliminium FIA – all stal nierdzewna 316 |
| --- | --- |
| Punkt aktywacji | LM1 – 1 actuation point N.C./N.O. contact LM2 – 1 actuation point SPDT contact LMM1 – 2 Punkt aktywacji N.C./N.O. contacts |
| Mocowanie | Ø 52 flange |
| Electrical connection | DIN 43650 – PG09 – IP65 |
| Switching capacity | LM1/LMM1 - 60W/VA LM2 – 30W/VA |
| Current | LM1/LMM1- 0,8A (resistive) LM2 - 0,5A (resistive) |
| Max voltage | 220V – 50Hz |
| Temperature range | -10°C +80°C |
| Max. ciśnienie | 10 bar |
| Fluid specific weight | ³ 0.7 |
| Fluid viscosity | 150 cSt |
| Certification and approvals | - - |
| Size | Max possible length 1500mm |

LM1 / LM2 / LMM1 FIA - TIA - PTIA - Stainless Steel Execution

TECHNICAL DATA

| Materials of construction | Stem: brass Float: NBR Mocowanie: thermoplastic |
| --- | --- |
| Punkt aktywacji | LM1 – 1 actuation point N.C./N.O. contact LM2 – 1 actuation point SPDT contact LMM1 – 2 Punkt aktywacji N.C./N.O. contacts |
| Connection | CFPA – Ø 54 flange CTPA – G1” thread connection |
| Electrical connection | DIN 43650 – PG09 – IP65 |
| Switching capacity | LM1/LMM1 - 60W/VA LM2 – 30W/VA |
| Current | LM1/LMM1- 0,8A (resistive) LM2 - 0,5A (resistive) |
| Max voltage | 220V – 50Hz |
| Temperature range | -10°C +80°C |
| Max. ciśnienie | 10 bar |
| Fluid specific weight | ³ 0.7 |
| Fluid viscosity | 150 cSt |
| Certification and approvals | - - |
| Size | Max possible length 1500mm |

LM1 / LM2 / LMM1 GSA - GSIA - Level Switches with Stop Ring

TECHNICAL DATA

| Materials of construction | GSA – brass stem, NBR float GSIA – all stal nierdzewna 316 |
| --- | --- |
| Punkt aktywacji | LM1 – 1 actuation point N.C./N.O. contact LM2 – 1 actuation point SPDT contact LMM1 – 2 Punkt aktywacji/floats N.C./N.O. contacts |
| Mocowanie | G3/8” |
| Electrical connection | 500mm leads (standard) |
| Switching capacity | LM1/LMM1 – 60W/VA LM2 - 30W/VA |
| Current | LM1/LMM1- 0,8A (resistive) LM2 - 0,5A (resistive) |
| Max voltage | 220V – 50Hz |
| Temperature range | -10°C +80°C |
| Max. ciśnienie | 10 bar |
| Fluid specific weight | ³ 0.7 |
| Fluid viscosity | 150 cSt |
| Certification and approvals | - - |
| Size | Max possible length 2500mm |

LM3 / LM4 GSA - GA - GTA - Level Switches with 3 lub 4 Floats

TECHNICAL DATA

| Materials of construction | Stem: brass Float: NBR Mocowanie: GSA – brass GA/GTA – anodized aluminium |
| --- | --- |
| Punkt aktywacji | LM3 – 3 Punkt aktywacji/floats N.C./N.O. contacts LM4 – 4 Punkt aktywacji/floats N.C./N.O. contacts |
| Mocowanie | GSA – G3/8” thread connection GA – Ø 92 flange GTA – G2” thread connection |
| Electrical connection | GSA – 500mm leads (standard) GA/GTA – 92x92mm junction box– PG09 – IP65 |
| Switching capacity | 60W/VA |
| Current | 0,8A (resistive) |
| Max voltage | 220V – 50Hz |
| Temperature range | -10°C +80°C |
| Max. ciśnienie | 10 bar |
| Fluid specific weight | ³ 0.7 |
| Fluid viscosity | 150 cSt |
| Certification and approvals | GA and GTA executions: RINA - Lloyd’s Register - Germanischer Lloyd |
| Size | Max possible length 2500mm |