PMN - Diaphragm/Piston Adjustable Pressure Switches

TECHNICAL DATA

| Switch rating | 0,5(0,2)A / 48 Vac-dc |
| --- | --- |
| Electrical connection | 6,3x0,8 |
| Adjusting range | 0.1…1 bar; 0.15...2 bar; 2...10 bar, 10...20 bar; 20...50 bar, 50...80 bar; 50...150 bar; 100...250 bar; 50...300 bar |
| Max static pressure | 80 bar, 150 bar, 300 bar, 400 bar, 600 bar (according to the possibile Zakres ciśnienia and the body material) |
| Hysteresis | Fixed |
| Temperatura pracy | -25°C ... +140°C (according to diaphragm/piston seal material) |
| Contact (without pressure) | N.O. or N.C. |
| Body material | Brass (standard) – Tropicalized Steel (standard) 303 Stainless Steel – stal nierdzewna 316 |
| Diaphragm/Piston seal | NBR (standard) – FKM – Silicone – HNBR – Neoprene – EPDM – Stainless Steel |
| Threads | Taper: G1/8” (standard) – G1/4” – M10x1 Parallel: M12x1,5 – G1/4” |
| Protection | IP00 (terminals) IP54 (with CAP1 and CAP10) |
| Mechanical life | 106 operations |
| Size | Body 24 AF Max height 54 mm |
| Certifications and Approvals | CE |
| Options | Set-point adjustment rising – Set-point adjustment falling – Gold contacts – Degreasing for oxygen applications – Gas test – High pressure execution – IP67 protection – Special thread connections |

PROTECTION CAPS

| CAP1 Protection: IP54 Material: NBR - FKM - EPDM | CAP10 Protection: IP54 Material: NBR |
| --- | --- |