TB/TBM - Bimetallic Temperature Switches Fixed Set-point

TECHNICAL DATA

| Switch rating | 10A / 240Vac |
| --- | --- |
| Electrical connection | końcówka śrubowa |
| Working temperature | 25°C–31°C–38°C–47°C-60°C–70°C–80°C-90°C-105°C |
| Tolerance | ± 5°C |
| Differential | Max 16°C |
| Max temperature | 120°C |
| Max. ciśnienie | 10 bar |
| Contact | N.O. (standard) – N.C. ( on request ) |
| Body | Brass |
| Thread connection | G3/8” – G1/2” |
| Protection | IP54 IP65 (with CAP2) |
| Size | Body 27 AF Height 57mm (TB series) Height 66mm (TBM series) |
| Options | Execution with optional magnet |

PROTECTION CAPS

CAP2 Protection: IP65 Cable clamp: G 3/8" Material: Nylon

TBP - Bimetallic Temperature Switches Fixed Set-point

TECHNICAL DATA

| Switch rating | 1(0,5)A / 220Vac |
| --- | --- |
| Electrical connection | końcówka śrubowa |
| Working temperature | 30°C-40°C-50°C-60°C-70°C-80°C-90°C-100°C-105°C |
| Tolerance | ± 5°C |
| Differential | Max 7°C |
| Max temperature | 120°C |
| Max. ciśnienie | 10 bar |
| Contact | N.O. – N.C. |
| Body | Brass |
| Thread connection | G1/4” – G3/8” – G1/2” |
| Protection | IP65 (with CAP2) |
| Size | Body 27 AF Height 71mm |
| Options | Threads: M12x1,5 – M14x1,5 – M18x1,5 – M22x1,5 |

PROTECTION CAPS

CAP2 Protection: IP65 Cable clamp: G 3/8" Material: Nylon

TBS - Bimetallic Temperature Switches Fixed Set-point

TECHNICAL DATA

| Switch rating | 1(0,5)A / 220Vac |
| --- | --- |
| Electrical connection | 6,3x0,8 |
| Working temperature | 30°C-40°C–50°C-60°C-70°C-80°C-90°C-100°C-105°C |
| Tolerance | ± 5°C |
| Differential | Max 7°C |
| Max temperature | 120°C |
| Max. ciśnienie | 10 bar |
| Contact | N.O. – N.C. |
| Body | Brass |
| Thread connection | G1/4” – G3/8” – G1/2” |
| Protection | IP54 (with CAP1 or CAP10) |
| Size | Body 24 AF Height 63,5mm |
| Options | Threads: M12x1,5 – M14x1,5 – M18x1,5 – M22x1,5 |

PROTECTION CAPS

| CAP1 Protection: IP54 Material: NBR – FKM – EPDM | CAP10 |
| --- | --- |

TBF - Bimetallic Temperature Switches Fixed Set-point

TECHNICAL DATA

| Switch rating | 10A / 240Vac |
| --- | --- |
| Electrical connection | 6,3x0,8 |
| Working temperature | 25°C–31°C-38°C-47°C-60°C-70°C-80°C-90°C-105°C |
| Tolerance | ± 5°C |
| Differential | Max 16°C |
| Max temperature | 120°C |
| Max. ciśnienie | 10 bar |
| Contact | N.O. – N.C. |
| Body | Brass |
| Thread connection | G3/8” – G1/2” |
| Protection | IP54 (with CAP1 or CAP10) |
| Size | Body 24 AF Height 40,5mm |
| Options | IP67 protection |

PROTECTION CAPS

| CAP1 Protection: IP54 Material: NBR – FKM – EPDM | CAP10 Protection: IP54 Material: NBR |
| --- | --- |

NTB/NTBM - Bimetallic Temperature Switches Fixed Set-point

TECHNICAL DATA

| Switch rating | 10A / 240Vac |
| --- | --- |
| Electrical connection | DIN 43650 – PG09 (swivel plug) |
| Working temperature | 25°C-31°C-38°C-47°C-60°C-70°C-80°C-90°C-100°C-105°C |
| Tolerance | ± 5°C |
| Differential | Max 16°C |
| Max temperature | 120°C |
| Max. ciśnienie | 10 bar |
| Contact | N.O. – N.C. |
| Body | Red anodized aluminium (standard) |
| Thread connection | G3/8” – G1/2” – M22x1,5 |
| Protection | IP65 |
| Size | Body 27 AF Height 74mm (NTB series) Height 84mm (NTBM series) |
| Options | Execution with optional magnet Brass body |

NTBC - Bimetallic Temperature Switches Fixed Set-point

TECHNICAL DATA

| Switch rating | 1(0,5)A / 220Vac |
| --- | --- |
| Electrical connection | DIN 43650 – PG09 |
| Working temperature | 30°C-40°C-50°C–60°C-70°C-80°C-90°C-100°C-105°C |
| Tolerance | ± 5°C |
| Differential | Max 7°C |
| Max temperature | 120°C |
| Max. ciśnienie | 10 bar |
| Contact | N.O. – N.C. |
| Body | Anodized aluminium (standard) |
| Thread connection | G3/8” – G1/2” – M22x1,5 |
| Protection | IP65 |
| Size | Body 24 AF Height 97mm |
| Options | Brass body |

EBT - Bimetallic Temperature Switches Fixed Set-point

TECHNICAL DATA

| Switch rating | 10A / 250Vac |
| --- | --- |
| Electrical connection | DIN 43650 – PG09 |
| Working temperature | 30°C-40°C–50°C–60°C-70°C-80°C-90°C-100°C-105°C |
| Tolerance | ± 5°C |
| Differential | Max 15°C |
| Max temperature | 130°C |
| Max. ciśnienie | 10 bar |
| Contact | N.O. – N.C. |
| Body | Brass |
| Thread connection | G3/8” – G1/2” – M22x1,5 |
| Protection | IP65 |
| Size | Body 30 AF Height 80mm |
| Options | - - |

EBC - Temperature Switches with C/O SPDT Contact

TECHNICAL DATA

| Switch rating | 1A / 24Vac |
| --- | --- |
| Electrical connection | DIN 43650 – PG09 |
| Working temperature | 30°C-40°C–50°C–60°C-70°C-80°C |
| Tolerance | ± 5°C |
| Differential | Max 15°C |
| Max temperature | 80°C |
| Max. ciśnienie | 10 bar |
| Contact | SPDT |
| Body | Brass |
| Thread connection | G3/8” – G1/2” – M22x1,5 |
| Protection | IP65 |
| Size | Body 30 AF Height 90.2mm |
| Options | - - |