IF...VE - Adjustable Electric Flow Switches with Visual Indication

TECHNICAL DATA

| Tempo przepływu | 0,1…60 LPM H2O |
| --- | --- |
| Materials | Anodized aluminium – Nickel-plated brass – 304 stainless steel Tube: Pirex glass Sealing: NBR (standard) - FKM - EPDM |
| Max. ciśnienie | 15 bar |
| Temperatura pracy | -10°C +100°C with NBR sealing |
| Intervention differential | ca. 20% |
| Electrical connection | DIN 43650 – PG09 – IP65 |
| Contact (dry) | N/O (standard) SPDT (only on request) |
| Switching voltage | DC: 60W / AC: 60VA |
| Max voltage | 220V – 50Hz |
| Current | 0,8A (resistive) |
| Size | IF1/IF2/IF3 – 136x40x40 mm IF4 – 163x40x40 mm IF5 – 190x50x50 mm |
| Thread connection | IF1/IF2/IF3 – G1/4” IF4 – G1/2” IF5 – G1” |
| Mocowanie | Vertical |
| Options | Different springs suitable for fluids more viscous than water |

IF...V2E - Adjustable Electric Flow Switches with Visual Indication

TECHNICAL DATA

| Tempo przepływu | 0,1…60 LPM H2O |
| --- | --- |
| Materials | Anodized aliminium – Nickel-plated brass – 304 stainless steel Tube: Pirex glass Sealing: NBR (standard) - FKM - EPDM |
| Max. ciśnienie | 15 bar |
| Temperatura pracy | -10°C +100°C with NBR sealing |
| Intervention differential | ca. 20% |
| Electrical connection | DIN 43650 – PG09 – IP65 |
| Contact (dry) | N/O (standard) SPDT (only on request) |
| Switching voltage | DC: 60W / AC: 60VA |
| Max voltage | 220V – 50Hz |
| Current | 0,8A (resistive) |
| Size | IF1/IF2/IF3 – 136x40x40 mm IF4 – 163x40x40 mm IF5 – 190x50x50 mm |
| Thread connection | IF1/IF2/IF3 – G1/4” IF4 – G1/2” IF5 – G1” |
| Mocowanie | Vertical |
| Options | Different springs suitable for fluids more viscous than water |

IF...DE - Adjustable Electric Flow Switches

TECHNICAL DATA

| Tempo przepływu | 0,1…140 LPM H2O |
| --- | --- |
| Materials | Anodized aluminium – Nickel-plated brass – 304 stainless steel Sealing NBR (standard) – FKM - EPDM |
| Max. ciśnienie | 150 bar |
| Temperatura pracy | -10°C +100°C with NBR sealing |
| Intervention differential | ca. 20% |
| Electrical connection | DIN 43650 – PG09 – IP65 |
| Contact (dry) | N/O (standard) SPDT (only on request) |
| Switching voltage | DC: 60W / AC: 60VA |
| Max voltage | 220V – 50Hz |
| Current | 0,8A (resistive) |
| Size | IF1/IF2/IF3 – 136x40x40 mm IF4 – 163x40x40 mm IF5 – 190x50x50 mm IF6 – 200x70x70 mm |
| Thread connection | IF1/IF2/IF3 – G1/4” IF4 – G1/2” IF5 – G1” IF6 – G1 1/2” |
| Mocowanie | Vertical |
| Options | Different springs suitable for fluids more viscous than water |